## Slide 1
Array of Processing Elements (PEs); each PE has ALU-like functional unit that works on an operation every cycle.
Power-efficiency of several 10s of GOps/Sec per Watt!
  ADRES [HiPEAC ‘08]
  HyCUBE [DAC ‘17]
Coarse Grained Reconfigurable Arrays (CGRAs)
Mapping Loops on CGRAs
Performance Impact of Ad-Hoc Routing Strategies
Spilling to Distributed RFs
Performance Critically Depends on the Obtained Mapping
Mapping Problem = Routing Problem
  Routing is needed when the dependent operations are scheduled at a distant time, or operations cannot be mapped due to resource constraints.
Compiler Microarchitecture Lab, Arizona State University
Shail Dave, Mahesh Balasubramanian, Aviral Shrivastava
RAMP: Resource-Aware Mapping for CGRAs
A 4x4 CGRA with Local Register File and 2-D Mesh Interconnect
B = 0;
for(i=0; i<1000; i++)
{
A = B - 4;
B = A + L;
C = A * 3
D = C + 7;
}
a:
b:
c:
d:
Sample Loop
a
b
c
1
d
Data Dependency Graph (DDG)
Modulo Schedule
1
2
1
II = 2
a
i=0
b
c
a
d
i=1
time
1
2
3
Routing in an ad-hoc manner
DDG, Arch Description, Target II
Mapping
Place & Route
Scheduling (IMS)
- EMS [H. Park et al., PACT ’08]
- EPIMap [M. Hamzeh et al., DAC ‘12]
Since ar is not rescheduled, cannot route a → e
Routing Data Dependency via PEs
e
a
b
d
c
DDG
1
3
1
2
2
time
1
2
d
a
3
e
c
P&R
b
ar
?
Schedule (II=3)
Routing via Registers
e
f
d
g
b
c
a
2
h
time
t
t+1
t+3
c
d
a
b
i
t+2
t+4
ei-1
ei
e
f
ei-1
ei-1
ei-1
t+5
h
g
?
ei-1
a
i+1
- Iterative Modulo Scheduling [B. Rau, MICRO ‘94]
  Software Pipelined Execution
Challenges with Code Generation Heuristics Employing Ad-hoc Routing Strategies
RAMP: Resource-Aware Mapping Technique
Routing
Strategy
1
2
3
Re-Schedule
Place & Route
Failure Analysis
Partition Mapping Problem in 3 Sub-Problems
Systematically and Flexibly Explore Resources to Achieve Mapping, Adapting to the Application Needs
  E.g. we can choose to first map the DDG with routing via registers. Then, for any unmapped data dependency, explore different routing options, per failure analysis.
Modulo Schedule DDG (Arch., II)
Generate Compatibility Graph CG
P&R (Find Maximal Clique of CG)
For Each Unmapped Node v/Edge e
Re- Compute
Graph Modification
Exhaustive Resource Exploration
Place & Route
All Operations Mapped?
Yes
No
A
B
C
G
F
Modified & rescheduled DDG
H
b
e
a
f
c
d
g
1
Total Loops Mapped
Speedup
0
5
10
0
20
10
4
8
12
Architecture Configuration
Resources
RAMP
Increase in
REGIMap
MEMMap
Done
Re-schedule
Load Read-Only Data
Is pred(v) live-in?
Ops Scheduled at Consequent Time?
Route via PEs
and/or Reg.
Dependent Ops Scheduled Far?
E
Failure Analysis
D
Spill to distrib. RFs
Select the Strategy that Uses Minimum Resources
Spill to Mem
Route via PE
Change Schedule Time
Experimental Setup
Routing via Memory
REGIMap [M. Hamzeh al.,DAC ’13]
GraphMinor [L. Chen et al., TRETS ‘14] Cannot efficiently utilize distributed RFs to route ei-2 → ai
Chart: Benchmarks
| sha | bitcount | susan_smooth | adpcm_enc | gsm_short | gsm_long | jpeg_enc | adpcm_dec | geomean
MEMMap | 0.33333 | 1 | 0.16667 | 1 | 0.18293 | 0 | 0.25 | 0.33333 | 0.36401
REGIMap | 0.42857 | 1 | 0.33333 | 1 | 0.24194 | 0.28571 | 0.4 | 0.54545 | 0.46416
RAMP | 1 | 1 | 1 | 1 | 0.83333 | 0.83333 | 0.66667 | 1 | 0.90822
gsm_ short
gsm_ long
susan_ smooth
geo mean
jpeg _enc
adpcm _enc
sha
bitcount
adpcm _dec
Higher the Better
0.91
time
t
t+1
t+3
c
d
a
b
i
t+2
t+4
ei-1
ei
e
f
ei-1
ei-1
ei-1
t+5
h
g
f
err
ei-2
ei-2
ei-1
ei-1
erw
a
ei
II = 5
ei-1
ei-2
e
f
d
g
b
c
a
2
h
8 MiBench benchmarks (top performance-critical loops)
RAMP modeled using CCF Compilation & Simulation Framework Available at: https://github.com/cmlasu/ccf (LLVM 4.0 and gem5 as foundation)
  CGRA modeled as a separate core coupled with ARM Cortex-like core
Evaluation over 12 architectural configurations
  PEs connected in a 2D torus, perform fixed-point computations
  CGRA accesses 4 kB data memory and 4 kB instruction memory
  Configurations vary in terms of array size, PE functionality, registers etc.
RAMP Improves CGRA’s Acceleration Capability by 2.13x
Acknowledgements
This work was partially supported by funding from NSF grants CNS 1525855 and CCF 172346 - NSF/Intel joint research center for Computer Assisted Programming for Heterogeneous Architectures (CAPA).
MEMMap [S. Yin al., TVLSI ’16] Statically determine the dependencies routed via memory
≠ spill data to memory when required (unavailability of regs)
time
1
2
4
3
5
6
c
b
d
a
i
e
f
g
lb
la
?
sa
sb
?